## Slide 1: Welding

## Slide 3: HMS (HSE)

## Slide 4: Fire safety
All must have read the hot work instructions
Must know where the fire extinguishers are
Must know that welding creates immense heat and nearby items might ignite

## Slide 5: Other HSE
Use extractor fan, keep it close. Otherwise you will inhale heavy metals
Use the correct gloves for the correct task
  Precision -> thinner gloves
  Heat management -> thicker gloves
The electrode can shock you (if you manipulate the torch with it on) and will get warm during use

## Slide 6: Setup

## Slide 7: TIDY THE BENCH
Please

## Slide 8: Equipment setup
Sharpen electrodes
Connect the machine and check settings
The clamp goes beneath the table
Get the correct fill metal (Aluminium vs steel, thickness)
Clean your workpiece (grind off and use potentially use IPA)
Secure material to bench as necessary
Turn on the exhaust fan
Close the curtains and switch to “opptatt” (occupied)

## Slide 9: Polarity

## Slide 11: The mask
Two types, fixed-shade and automatics
We only use automatics
Adjust so you can see well, without discomfort

## Slide 12: Covering up
The light from the arc can do more than blind you
Always cover your skin, or you will have massively increased risk of skin cancer
Coverall works well, especially use if your clothes contain plastic

## Slide 13: Technique

## Slide 14: Is sex-appeal the goal?

## Slide 15: No, we want strength

## Slide 16: How to achieve appropriate penetration
Sharp electrode
Correct settings
Correct distance
Correct angle
Correct movements

## Slide 17: What makes for a good weld?

## Slide 18: Sharp electrodes
The angle determines the penetration
Sharper is wanted, to a point. 50-60 degrees works well

## Slide 19: Correct settings
A balance between amps (heat) and movement speed

## Slide 20: Pre- and postflow
Preflow is for cleaner starts
Postflow is to stop inclusions when instantly shutting off gas
No need to overdo it, we do not need to waste gas.
Pre: 1-2 seconds
Post: 4-7 seconds

## Slide 21: Correct distance
Too far away – shallow penetration
Too close – might touch and cake/stuck the electrode
Balance is needed – 1 to 5 millimeters is a good range
Look at the arc, if it is wide or moves erratically, move closer

## Slide 22: Correct angle and movements
This is the hard part
Experience teaches well
But some base rules are good:
  Simple lines work for simple work (butts, maybe laps)
  For better welds and more complex work, use a zig-zag motion or similar
In the end it all boils down to…

## Slide 23: The puddle
Read it, learn it and make it your friend

## Slide 25: Welding well means loving the puddle
Never leave your puddle, it is your weld
  The puddle follows the heat, so the tip of your electrode
Puddle too small, fill more
Puddle too big, move more or check distance
Puddle sinking, move more or reduce heat
Keep watch of the puddle’s consistency
  If it becomes matt, it is not hot enough
  Bad puddle consistency -> bad welds

## Slide 26: Do you see how the puddle has moved?

## Slide 27: Further potential learning
Ignore if only running basics

## Slide 28: Aluminium welding
Hard, more to think about than steel or even stainless
AC needed (DCEP possible, but discouraged due to electrode eating tendencies)
  This is due to the oxidization of aluminium
  We need to remove the oxide before welding
  Current pulls the oxide off

## Slide 29: Pedal welding
For precise heat control throughout a weld

## Slide 30: When you’re done welding
Turn off the machine
Turn off the gas
Let the workpiece cool down (stay at the workshop a minimum of 1 hour and check)
TIDY UP AFTER YOURSELF